## Slide 1: Monitoring trees outside the forest
World resources institute
John Brandt

## Slide 2: Issues in monitoring trees outside forest
Low resolution of imagery
High background variability and noise
Small object size
Sub 10m shifts in georeferencing
Hill shade and terrain
Traditional ML approaches on GEE are not expressive enough (RF)
Out of box computer vision approaches do not work because of small image size, variability of data, and variability of segmentation maps

## Slide 3: Going out of the forests
While current forest monitoring data is great at forest monitoring, it is not tailored to monitoring restoration outside the forest
  False positives in grasslands and crops
  False negatives in mosaic landscapes
Wall-to-wall restoration monitoring must prioritize accuracy on heterogenous landscapes, rather than homogenous landscapes
Proposing complimentary data to monitor trees outside the forest

## Slide 4
Trees look like grass
Trees look like crops
Scattered trees have variable backgrounds

## Slide 7: Why out-of-box algorithms fail
1 million + pixels
Shapes consistent
Regions consistent
Colors consistent
196 pixels
No shape, region, or color consistency
Each output is distinct

## Slide 8: DATA
700 2 hectare plots
Randomly sampled across Tigray, Ethiopia

## Slide 9: Quick DEMO
Link

## Slide 11: Methods - Preprocessing
Data selection
  Biweekly mean composites of 10 and 20m bands
  2 images / month with lowest cloud cover, capped at 20%
  Bilinearly interpolate missing imagery
  Normalize data to [0, 1] range
  Fuse slope calculated from DEM to S2
Georeference correction
  Expectation maximization

## Slide 12: Methods - Modeling
Fully convolutional network with:
Convolutional LSTM encoder with layer normalization and zone out
Feature pyramid attention between encoder and decoder with DropBlock
Concurrent spatial and channel squeeze excitation decoder
AdaBound optimizer
Focal loss for a warm-up, fine tuned with Lovasz softmax. Focal loss is tuned (gamma and alpha) for each image.
Equibatch sampling, visiting every C clusters each N samples

## Slide 13: Modeling Spatiotemporal relationships
Generate 24 different “feature maps” that represent how 30x30m grids of the plot change over the year
Weight the 24 different feature maps by how relevant they are to disambiguating trees from background
Convolutional LSTMs allow for the representation of temporal and temporal relationships concurrently

## Slide 14: Incorporating long-distance context
To optimize single pixel accuracy while modeling long distance relationships:
  Feature pyramid attention (+4%)
  Adabound optimizer (+3%)
  Hypercolumn decoder (+2%)
  cSSE blocks (+1%)

## Slide 15: Sampling methods, Regularization
Stratified sampling
Equibatch (+5%)
Layer norm, batch re-norm (+1%)
L2 loss (+0.5%)
Zone out (+3%)
Data augmentation (+3%)
Heavy gradient clipping

## Slide 16: Metrics
Prediction speed: 312,000 ha/hour/core
Model parameter size: 90,000 (vs. 60M-130M+ in out of box algorithms) – 600-1400x faster
Map of Ethiopia, 16 core VM / K80 GPU @ $0.48 / hour (above fixed cost of data IO)
  This approach: 20 hours / $9
  DeepLab V3: 36 months / $12,441
  PSPNet: 13 months / $4,416
Suggests ability to detect 2% tree cover difference at 2 ha scale outside of forests
Tree cover % | Precision @ 10 m | Recall @ 10 m | Percent error @ 2 ha
50+ | 90% | 88% | 2%
20-50 | 68% | 70% | 2%
<20 | 45% | 68% | 2%
Overall | 65% | 72% | 1.60%

## Slide 17: Test plots
200 2 ha plots across 8 million km2 in
  Ethiopia
  Sudan
  South Sudan
  Djibouti
  Somalia

## Slide 18: Success cases failures

## Slide 19: Future research directions - methods
S1 S2 fusion
Atruous convolutions
Better data augmentation
Hyperparameter search
Regularization search
Self training
Stratified K-fold training and ensembling
Temporal squeeze and excitation
Post processing – smoothing and conditional random fields

## Slide 20: Future research directions - applications
Short term: 50,000 hectare -> 500,000 hectare maps (regional)
Medium term: Multi-year imagery and tree cover change
Long term: Other biomes and geographic regions

## Slide 21: Conclusions and questions
Complimentary research product to existing forest monitoring data and methodologies, focusing on trees outside the forest by using artificial intelligence to focus attention on disambiguating trees from crops and grassland with a methodology that is computationally scalable to global levels
Still in research stage but performs well on 30-50,000 ha mosaic landscapes with only 1,000 ha of labeled data
Issues of hill shade, georeferencing shifts, data quality are actively being mitigated
  Azimuth correction
  Expectation maximization
  Label smoothing, teacher networks
  Post-processing
Expect regional 500,000 to 1,000,000 ha maps across priority drylands area within next year